## Slide 1
BRACE2: Bridge Rapid Assessment Center
for Extreme Events
Principal Investigator: Khalid M. Mosalam, UC Berkeley Student Investigators: Claudio Perez & Chrystal Chern, Researchers, UC Berkeley University of California Berkeley
objective: invert the conventional analysis problem
val, vec = eigid(inputs, outputs)
Two Approaches
Limitations
Solution
Application
SRIM
State space system identification techniques such as System Realization with Information Matrix reveal the underlying fundamental dynamic system for a multi-input, multi-output, or MIMO signal.
Optimizations
A new, optimized algorithm has been developed that leverages shared memory parallelism to drastically reduce the computational demands of estimating a state space model.
Memory use has been optimized to efficiently leverage caching.
Package
All methods are accessible through the python lilo package.
lilo.eigid(inputs, outputs)
Idea: Fit an ideal continuous system to the discrete response in the time domain.
Ho-Kalman/Eigensystem Realization Algorithm
Subspace Identification
Least Squares Methods
Idea: Represent the system in the frequency domain.
Fourier Spectrum
Response Spectrum
High complexity systems
Frequency domain methods are ill-suited for identifying higher modes, and are limited to single-input, single-output, or SISO signals.
SVD
The singular value decomposition is heavily used in subspace and least squares methods. It is notoriously numerically intensive.
Identification methods must be scalable such that they can be applied to a growing and changing network of bridges.

## Slide 2
BRACE2: Bridge Rapid Assessment Center
for Extreme Events
Principal Investigator: Khalid M. Mosalam, UC Berkeley Student Investigators: Claudio Perez & Chrystal Chern, Researchers, UC Berkeley University of California Berkeley
objective: invert the conventional analysis problem
val, vec = eigid(inputs, outputs)
Two Approaches
Limitations
Solution
Application
SRIM
State space system identification techniques such as System Realization with Information Matrix reveal the underlying fundamental dynamic system for a multi-input, multi-output, or MIMO signal.
Optimizations
A new, optimized algorithm has been developed that leverages shared memory parallelism to drastically reduce the computational demands of estimating a state space model.
Memory use has been optimized to efficiently leverage caching.
Package
All methods are accessible through the python lilo package.
lilo.eigid(inputs, outputs)
Idea: Fit an ideal continuous system to the discrete response in the time domain.
Ho-Kalman/Eigensystem Realization Algorithm
Subspace Identification
Least Squares Methods
Idea: Represent the system in the frequency domain.
Fourier Spectrum
Response Spectrum
SVD
The singular value decomposition is heavily used in subspace and least squares methods. It is notoriously numerically intensive.
High complexity systems
Frequency domain methods are ill-suited for identifying higher modes, and are limited to single-input, single-output, or SISO signals.
Identification methods must be scalable such that they can be applied to a growing and changing network of bridges. That is, they must require minimal modification when applied to new assets, and they must be low-cost.

## Slide 3
BRACE2: Bridge Rapid Assessment Center
for Extreme Events
Principal Investigator: Khalid M. Mosalam, UC Berkeley Student Investigators: Claudio Perez & Chrystal Chern, Researchers, UC Berkeley University of California Berkeley
objective: invert the conventional analysis problem
val, vec = eigid(inputs, outputs)
Two Approaches
Limitations
Solution
Application
SRIM
State space system identification techniques such as System Realization with Information Matrix reveal the underlying fundamental dynamic system for a multi-input, multi-output, or MIMO signal.
Optimizations
A new, optimized algorithm has been developed that leverages shared memory parallelism to drastically reduce the computational demands of estimating a state space model.
Memory use has been optimized to efficiently leverage caching.
Package
All methods are accessible through the python lilo package.
lilo.eigid(inputs, outputs)
Idea: Fit an ideal continuous system to the discrete response in the time domain.
Ho-Kalman/Eigensystem Realization Algorithm
Subspace Identification
Least Squares Methods
Idea: Represent the system in the frequency domain.
Fourier Spectrum
Response Spectrum
SVD
The singular value decomposition is heavily used in subspace and least squares methods. It is notoriously numerically intensive.
High complexity systems
Frequency domain methods are ill-suited for identifying higher modes, and are limited to single-input, single-output, or SISO signals.
Network
Identification methods must be scalable such that they can be applied to a growing and changing network of bridges. That is, they must require minimal modification when applied to new assets, and they must be low-cost.

## Slide 4
BRACE2: Bridge Rapid Assessment Center
for Extreme Events
Principal Investigator: Khalid M. Mosalam, UC Berkeley Student Investigators: Claudio Perez, Chrystal Chern, Researchers, UC Berkeley University of California Berkeley
val, vec = eigid(inputs, outputs)
Two Approaches
Limitations
Solution
Application
Idea: Fit an ideal continuous system to the discrete response in the time domain.
Ho-Kalman/Eigensystem Realization Algorithm
Subspace Identification
Least Squares Methods
Idea: Represent the system in the frequency domain.
Fourier Spectrum
Response Spectrum
State space system identification with SRIM
Parallel
lilo.eigid(inputs, outputs)

## Slide 5
BRACE2: Bridge Rapid Assessment Center
for Extreme Events
Principal Investigator: Khalid M. Mosalam, UC Berkeley Student Investigators: Claudio Perez, Chrystal Chern, Researchers, UC Berkeley University of California Berkeley
val, vec = eigid(inputs, outputs)
Two Approaches
Limitations
Solution
Application
Idea: Fit an ideal continuous system to the discrete response in the time domain.
Ho-Kalman/Eigensystem Realization Algorithm
Subspace Identification
Least Squares Methods
Idea: Represent the system in the frequency domain.
Fourier Spectrum
Response Spectrum
State space system identification with SRIM
Parallel
lilo.eigid(inputs, outputs)

## Slide 6
BRACE2: Bridge Rapid Assessment Center
for Extreme Events
Principal Investigator: Khalid M. Mosalam, UC Berkeley Student Investigators: Claudio Perez, Chrystal Chern, Researchers, UC Berkeley University of California Berkeley
val, vec = eigid(inputs, outputs)
Two Approaches
Limitations
Solution
Application
Idea: Fit an ideal continuous system to the discrete response in the time domain.
Ho-Kalman/Eigensystem Realization Algorithm
Subspace Identification
Least Squares Methods
Idea: Represent the system in the frequency domain.
Fourier Spectrum
Response Spectrum
State space system identification with SRIM
Parallel
lilo.eigid(inputs, outputs)